COMPUTER NETWORKS PROJECT

Implementation and Simulation of Go-Back-N and Selective Repeat Protocols
Submitted By:- Submitted To:

Sarthak Thapliyal : 17103095 Dr. Taj Alam
Akash Gupta : 17103091 Dr. Shilpa Bhudkar
Abdus Samad : 17103074
Arpit Garg : 17103069

Implementation and Simulation of Go-Back-N and Selective Repeat Protocols

  UDP (User Datagram Protocol), defined in RFC 768 provides a connectionless and unreliable data transfer service between end users. Doing little beyond multiplexing and demultiplexing with addition of light error checking, it adds little to improve the unreliable data transfer service of the network layer protocol, IP. Unlike its counterpart, the Transmission Control Protocol, TCP, UDP doesn’t implement the technique of handshaking between sender and receiver before initiating communication, (hence, connectionless). Neither does it provide a reliable data transfer service through ACK’s and sequence numbers. These limitations however, are advantages for some applications like Internet Telephony and other loss-tolerant applications. With UDP providing greater control over data transmission as it almost immediately transmits data sent by the application utilizing it thus, TCP’s retransmission mechanism which is quite favourable for loss – tolerant applications, it also skips TCP’s handshaking mechanism for connection establishment along with congestion and flow control, all of which could lead to unnecessary latencies for applications that demand immediate data transmission.
Switching on to protocols that provide reliable data transfer service, Go-Back-N (GBN), also known as sliding window protocol, has been implemented as an enhancement rdt (reliable data transfer 3.0) protocol. Allowing sender to transmit multiple packets without waiting for an acknowledgement, the former is constrained by the window size N which defines the maximum number of unacknowledged segments with each segment in the window being assigned a unique sequence number, in accordance to which an ACK shall be sent by the receiver. With a timer implemented at the sender, retransmission of the entire window shall be initiated upon the event of timeout.
Selective Repeat (SR) is another example of a protocol providing reliable data transfer service while attempting to mitigate the disadvantages of Go-Back-N which can potentially lead to large retransmissions in case of timeout. Incorporating a transmitting window for packets in a similar manner to Go-Back-N, the Selective repeat however, does not provide cumulative but acknowledgements for individual segments. With timer implemented at sender, only the segment for which acknowledgement was not received shall resent in the event of a timeout, thereby reducing the Go-Back-N’s need of large retransmissions.
In this project, we have implemented, the two aforesaid reliable data transfer protocols i.e. GBN and SR over the unreliable transport layer protocol UDP. Mechanisms to demonstrate their robustness in events of errors such as checksum error, lost packets and ACKS’s have also been deployed in the program, the implementation of which has been undertaken in C language. The codes for both Client and Server have been written, implemented and tested on the Desktop version of the Linux Operating System’s 64-bit Ubuntu 17.10.1. Having completed writing the codes for both client and server in accordance with the requirements of the project and the useful tips provided for the same, the output, when the Server program was compiled and executed over the Linux terminal followed by the client, for the project requirements is as follows:
- Python2
- Socket programming
Giving the required inputs through the command line which included the input file, as per project requirements, we attempted to start the receiver.Giving the required inputs through the command line which included the input file, as per project requirements, we attempted to start the sender.
With both the client and server running the transmission has been initiated. As per project requirements, the segments being sent are displayed over the command line along with expected and received ACK’s.
Introducing error mechanism, entire windows one and three were retransmitted due to lost ACK or lost Packet, as per GBN’s retransmission mechanism.Introducing Checksum error mechanism for Packet 1, ACK of the packet last received correctly is being sent.ON the receiver side, as packet number 5 is incorrectly received ACK of packet 4 is sent, in the aftermath of which packet 5 is retransmitted.Giving the parameters through the command line to initiate transmission through the SR Protocol, thee sending and receiving is successful.
Introducing error mechanism in the form of lost ACK, the segment 1 was retransmitted as ACK wasn’t received before its timer expired.

Instructions for Execution of Program
Heading to the directory where the receiver program is stored from the terminal of Linux, execute the following line to run the server using SR protocol:
  - python2 server.py port_no SR window_size
Where,
port_no is the port number between 1025 and 65635
  1. Execute the client file using the following line:
  - python2 client.py filename port_no window_size
    Where,
      filename is name of configuration file

Screenshots